## Slide 1: BLE-IoT-Gwy
2018/11/23 Written
2019/01/02 Updated

## Slide 2: Introduction
BLE – Bluetooth Low Energy
  Radio technology with range of a few meters
  Bluetooth 4.0+ or once called Bluetooth Smart
IoT – Internet of Things
  Devices having Internet connectivity
This set of slides shows how BLE-capable devices can be part of Internet

## Slide 3: Bluetooth Classic (before 2010)
Mobile
PC
Internet
Keyboard
Mouse
Speaker
Headset
Closed connection between user and device

## Slide 4: Bluetooth LE (since 2010)
Mobile
Cloud
Sensors:
Health devices,
Temperature, etc.
Controllers:
Lights.
Air conditioner,
Doors, etc.
Requires Inetnet connection to be useful
PC

## Slide 5: BLE is designed for IoT
BLE/Gatt profile:
  modled after read/write to I/O ports
  allows small amount of data exchange in one or two packets
This indicates access to edge devices is a goal:
  Sensors
  Controllers (actuators)

## Slide 6: Gateway plays a Key role
Gateway
Sensor
BLE
Controller
BLE
Mobile
Cloud
PC

## Slide 7: BLE Mesh
Gateway
BLE
Cloud
BLE
BLE
BLE
BLE

## Slide 8: Connecting BLE to Internet
Mobile sends an HTTP request to BLE controller
  to operate a device at home.
BLE sensor sends an HTTP request to the cloud
  to allow PC or mobile to check status.
REST APIs for these purposes are proposed in Bluetooth SIG white papers
Bluetooth Meet The Internet Internet Say Hello To Bluetooth
https://blog.bluetooth.com/bluetooth-meet-the-internet-internet-say-hello-to-bluetooth

## Slide 9: Gateway Architecture
Cloud
BLE
Peripheral
HTTP
Server
HTTP
Client
BLE
Central
Scan
Write
Notification