## Slide 1: BLE-IoT-Gwy
2018/11/23 作成
2019/01/02 更新

## Slide 2: はじめに
BLE – Bluetooth Low Energy
  数メートルをカバーする無線技術
  Bluetooth 4.0+ または Bluetooth Smart とも
IoT – Internet of Things
  インターネットに接続可能なデバイス
以下では、BLEをインターネットに参加させる方法を考えてみる

## Slide 3: Bluetooth Classic (before 2010)
Mobile
PC
Internet
Keyboard
Mouse
Speaker
Headset
ユーザとデバイスの閉じた関係

## Slide 4: Bluetooth LE (since 2010)
Mobile
Cloud
Sensors:
Health devices,
Temperature, etc.
Controllers:
Lights.
Air conditioner,
Doors, etc.
有用となるにはネット接続が必要
PC

## Slide 5: BLE is designed for IoT
BLE/Gattプロファイルの特性
  I/Oポートの読み書きがモデル
  少量のデータの読み書きをパケット一往復で実現
↓
末端機器へのアクセスをめざしたことが理由
  センサー
  コントローラ（アクチュエータ）

## Slide 6: Gateway plays a Key role
Gateway
Sensor
BLE
Controller
BLE
Mobile
Cloud
PC

## Slide 7: BLE Mesh
Gateway
BLE
Cloud
BLE
BLE
BLE
BLE

## Slide 8: Connecting BLE to Internet
モバイル → HTTPリクエスト → BLEコントローラ
  家庭の機器を操作
BLEセンサ → HTTPリクエスト → クラウド
  PCやモバイルでチェック
このようなREST APIがBluetooth SIGのホワイトペーパで提案されている
Bluetooth Meet The Internet Internet Say Hello To Bluetooth
https://blog.bluetooth.com/bluetooth-meet-the-internet-internet-say-hello-to-bluetooth

## Slide 9: Gateway Architecture
Cloud
BLE
Peripheral
HTTP
Server
HTTP
Client
BLE
Central
Scan
Write
Notification